# Introduction
CIC filter is a filter for multirate digital signal processing. CIC filter-decimator performs low-pass filtering and decimation. CIC filter has economical architecture and uses registers, no multipliers required. Filter consists of chain of integrator stages and chain of comb stages.

# Structure of CIC filter
Structure of the CIC decimation filter, non-pipelined is shown on Figure 1.

Σ
z-1

Σ
z-M

-
+
Σ
z-1

Σ
z-M

-
+
...
...

fs
fs/R

Integrator section, N stages
Comb section, N stages
Figure 1: CIC decimator, non-pipelined.
Long chain of adders reduce speed performance. For reducing delays in the chain of adders this structure transformed to pipelined structure shown on Figure 2.

Σ
z-1

Σ
z-M

-
+

...
...

fs
fs/R

Integrator section, N stages

Comb section, N stages

z-1

Figure 2: CIC decimator, pipelined.
This structure is generated with parameter SMALL_FOOTPRINT=0
This structure requires half more registers with M=1 due to additional registers in comb part of filter.
But if R is large enough then no high speed in comb part required. If adder yields result for time less than Tsamp and after decimation period of sample is Tsamp*R then in comb part time to calculate every sample is R times more. If N is less than R then adders can be tied into chain without registers. This structure uses integrator part of pipelined structure and comb part of non-pipelined structure. Figure 3 shows this struscure.

fs
fs/R
Σ
z-M

-
+
Σ
z-M

-
+
...

Σ
z-1

...

Integrator section, N stages
Comb section, N stages
Figure 3: CIC decimator, combined.
This structure is generated with parameter SMALL_FOOTPRINT=1
# Frequency characteristics
Transfer function of the filter is
H( z )=( {{1-z^{RM}}over{1-z^-1}} )^N
Amplitude response
lline H (f) rline = ( {sin(%pi f M)} over {sin({%pi f} over {R})} ) ^N
# Bits pruning
If the number of bits in the input data stream is Binp , then first stage requires
B_max= left lceil N log_2(RM)+B_inp - 1 right rceil .
In next stages bits truncated according to Hogenauer bits pruning theory.
# References
Hogenauer, E. B., "An Economical Class of Digital Filters for Decimation and Interpolation",
IEEE® Transactions on Acoustics, Speech, and Signal Processing, Vol. ASSP-29, No. 2, April 1981,
pp. 155-162.
U. Meyer-Baese, Digital Signal Processing with Field Programmable Gate Arrays, 2nd Edition, Spinger, 2004, pp. 256-272.
https://www.so-logic.net/documents/trainings/03_so_implementation_of_filters.pdf